## Slide 1: EENG 284 Lab 7
Cellular Automata
Notes: Usually the <title of the lab> is what will be called the “System” through the rest of this document

## Slide 2: Lab Objectives
Logic
  Simple FSM
  Cellular automata
Verilog
  D flip flop
Simulation
Synthesis

## Slide 3: Theory
Collection of basic processing elements
Two states, alive (filled = black = 1) and dead (empty = white = 0)
  Models population dynamics
Next state depends on current state and two nearest neighbors states
Apply rule to each cell to determine next state
Notes: Replace <System> with the name of the

## Slide 4: Theory
Rules are numbered by the binary code of the next state
For example: 8’b01011010 = Rule 90
What is next state of cells under Rule 90?
  Assume that C7 left connects with C0 right
Notes: Replace <System> with the name of the

## Slide 5: Theory
What is next state of cells under Rule 90?
  Assume that C7 left connects with C0 right
C7 | C6 | C5 | C4 | C3 | C2 | C1 | C0
010 | 101 | 011 | 110 | 101 | 010 | 100 | 001
0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
Notes: Replace <System> with the name of the

## Slide 6: Theory
Rule 90 from a single cell
Notes: Replace <System> with the name of the

## Slide 7: Operation
Notes: Talk about the input is transformed into the output using the system architecture

## Slide 8: System Architecture

## Slide 9: singleCell module

## Slide 10: Switch Bouncing
Contacts of a switch physically bounce
Solution is to use SR latch
  sClk button to set input
  rClk button to reset input
If sClk bounces, just sets already set
If rClk bounces, just resets already reset
Two button presses for 1 clk period

## Slide 11: Deliverables
cellularAutomata Testbench (Rule 90 from a single cell)
Working cellularAutomata implementation on Cyclone V GX