## Slide 1: EENG 284 Lab 2
Hexadecimal to 7-segment converter
Notes: Usually the <title of the lab> is what will be called the “System” through the rest of this document

## Slide 2: Lab Objectives
Learn how the always/case statement implements truth tables.
How to combine bits into vectors.
How to download synthesized code the development boards.

## Slide 3: Cyclone V GX Board
Field Programmable Gate Array (FPGA)
  Cyclone V GX
User Inputs
  4 push buttons
  10 toggle switches
Outputs
  10 red LEDs
  8 green LEDs
  4 7-segment displays

## Slide 4: 7-segment Display
Consists of 7 active low light emitting diodes (LEDs)
  LEDs light up when you send them logic 0
  LEDs turn off when you send them logic 1
Illuminated to form characters 0-F
Notes: A light-emitting diode (LED) is a semiconductor light source that emits light when current flows through it.

## Slide 5: Hexadecimal to 7-segment converter
Input: 4-bit hexadecimal value (from slide switches)
Output: Pattern to illumination hex character
Notes: Replace <System> with the name of the

## Slide 6: Verilog: Vectors
Define a vector f
wire [2:0] f;
Assign a value using concatenation of 1-bit values
assign f = {a, b, c}; // a is MSB
Assign a value using a 3-bit vector
assign f = 3’b101;
Access a bit of a 3-bit vector. Indexed starting at 0
assign y = f[2]; // MSB of f vector
Notes: Talk about the input is transformed into the output using the system architecture

## Slide 7: Verilog: Always/Case statements
Implement truth tables
  always @(*)
    always/case is always running
  case (x)
    x is the input variable – usually a vector
  List of values of input are on left
  Output in right
    Pretty boring function

## Slide 8: Simulation
Perform simulation
  Checks for syntax errors
  Ensure hex2SevenSeg works

## Slide 9: Synthesis
Converts Verilog to Cyclone V GX fabric
Create association between
  hex2SevenSeg ports
  FPGA pins
FPGA pins are connected to Cyclone V GX inputs and outputs
Use Cyclone V GX User Manual
  Find I/O device
  Find letter/number code for cyclone pin

## Slide 10: Deliverables
Part 1:
  Truth Table for combinedLab01 function
  Timing diagram for combinedLab01 function
  Pin assignment for combinedLab01
Part 2:
  Truth Table for hexToSevenSeg function
  Verilog code for hexToSevenSeg function – just the always/case statement
  Simulation timing diagram for hexToSevenSeg function
  Pin assignment for hexToSevenSeg
  Demonstrate operation of hexToSevenSeg in lab